## Slide 1: Data prepared for student work
Olve Mo
Notes: Bildet illustrerer:
· bredden i SINTEFs ekspertise, fra havrom til verdensrom.
· hvilke områder og bransjer vi jobber innen for å realisere visjonen Teknologi for et bedre samfunn.
Bildestilen er basert på stikkordene fremtidsrettet, teknologi og norsk natur (naturressurser). SINTEFs visuelle univers er utviklet for SINTEF av Headspin Productions AS.

## Slide 2: Revision
Revision 01
Corrected measurement unit for fuel consumption. See slide 5 and 17
See new slide 6 with explanation of dpMode and operationId

## Slide 3: Summary
Data for one week of operation (168 hours):
  From 00:00h on January 30th to 23:59h on February 5th 2020
Covers three trips offshore and the beginning of a forth trip
Sample time: 1 second
Time vector is given in minutes relative to 00:00h on January 30st 2020
Data included:
  Battery power (power to the vessel grid)
  Sum consumed power for thrusters and propulsion
  Sum power to other loads on the vessel (calculated)
  Shore power (estimated/calculated)
  Number of engines running
  Sum power from diesel generators
  Power delivered from each of the four engines (4x)
  Instantaneous specific fuel consumption for each of the engines (4x)
  Instantaneous fuel consumption for each of the engines (4x)
  DP mode
  Operation mode Id

## Slide 4: Vessel latitude-longitude position, day by day.

## Slide 5: Measurement tags
Tag | Unit | Description
timeVectRelMinutes | Minutes | Time relative to 00:00h on January 30st 2020
battery_0_actualPower | kW | Power delivered from battery to vessel grid (negative for charging)
thrusterAndPropulsion | kW | Power consumed by thrusters and propulsion
hotelLoad | kW | Vessel hotel load: non-thrusters and propulsion loads such as accommodation and auxiliaries. Estimation used when connected to shore power.
sumEngMdoPower | kW | Sum power delivered from 4x diesel engines
shorePowerEstimated | kW | Estimated shore power delivered to vessel (Estimation based on records from shore)
engineMdoPower_x_ | kW | Power delivered from engine x (4x signals)
engineMdoPerformance_x_ | kg/MWh | Instantaneous specific fuel consumption for engine x
engineMdoConsumption_x_ | kg/h l/h | Instantaneous fuel consumption for engine x
numberOfMdoEnginesRunning | - | Number of engines running
operationId | - | Type of operation (se next page)
dpMode | - | Dynamic positioning mode (see next page)

## Slide 6: operationId / dpMode
operationId has the following interpretation
  Other = 0,
  Port = 1,
  Maneuver = 2,
  Transit_Eco = 3,
  Transit = 4,
  Transit_Fast = 5,
  Port_ShoreConnection = 6,
  Standby = 7,
  Port_Battery = 8,
  DP_Standby = 100,
  DP_Class2 = 101,
  DP_Gangway = 102,
  DP_Maneuver = 103
dpMode has the following interpretation
  0 = no dp mode.
  1 = standby/station keeping.
  2 = manevering

## Slide 7: Hotel load remarks
Hotel load is all loads except for thrusters and propulsion
The hotel load is not actually measured, it is in the logging system calculated based on thruster, propulsion, engine and battery power
The real measurements are not necessarily perfectly synchronized, and somewhat different filtering is probably applied in the different systems
For measurements with 1 second sampling this can give some strange results in calculated hotel load when power flow for engines, battery and thrusters changes fast
The consequence: Hotel load may look a bit strange during fast transients, e.g. going to zero or below for short periods. In reality, the hotel load will be less oscillating than what appears on the plots and will in reality never be zero.

## Slide 8: Hotel load remarks (cont.)
As explained on previous slide, the hotel load are a calculated value. The way the calculation is carried out in the logging system gives apparently zero power consumption while vessel is on shore power since the system does not know about the shore power. This is however not correct since there will always be some consumption onboard.
A realistic value to assume for shore power and onboard consumption while on shore power is 250kW based on recordings from shore measurements provided by Havilla (need to estimate since only average values each month available)
Thus, in the data prepared and shown here, 250kW is assumed to be the hotel load whenever the vessel is supplied from shore
The criteria's used to assume that vessel is fully, or partly, supplied from shore are:
  No engine running
  Engine running but engine load less than 100kW

## Slide 9: Shore power remarks
Power from shore is not measured by the onboard logging systems. The energy from shore is therefore not available in the logged data.
The criteria's used to assume that vessel is fully, or partly, supplied from shore are:
  No engine running
  Engine running but engine load less than 100kW (assumes generator runs in parallel to shore connection)
The shore power in the provided data has then been estimated as :
  shore power = (estimated hotel load) – (battery system power) - (engine power)
The way the hotel load and shore power is estimated ensures consistency such that
  (engine power)+ (shore power)+ (battery system power) -(estimated hotel load) – (Thrust.&prop.load) = 0

## Slide 10: Power flow overview

## Slide 11: Main power flows

## Slide 12: Power delivered from battery to vessel grid

## Slide 13: Number of running engines

## Slide 14: DP mode and Operation id

## Slide 15: Output power for each of the four engines

## Slide 16: Engine specific fuel consumption (kg per MWh)
Error in all y-axis legends: Should be kg/MWh

## Slide 17: Engine fuel consumption (per hour)
NOTE: New information:
Y-axis is
liter/hour
(not kg/hour)
Default conversion factor used the logging system is 0.865 kg/l

## Slide 18: Vessel position each hour (day 1 and 2)

## Slide 19: Vessel position each hour (day 3 and 4)

## Slide 20: Vessel position each hour (day 5 and 6)

## Slide 21: Vessel position each hour (day 7)

## Slide 22: Files on the shared folder (Microsoft Onedrive)
Data for student work.ppt
  This presentation
dataTableStudents.mat
  All data on Matlab format
  Contains the Matlab table "dataTableStudents"
  Note: The Matlab syntax for tables need to be used to access the data. Use table2array or table2struct if you prefer to work with other formats
dataTableStudents_I.xlsx
  Data on Excel format
  Contains all but the fuel consumption data
dataTableStudents_II.xlsx
  Data on Excel format
  Contains the time vector and the fuel consumption data